## Slide 1
Analysis
Not pleasing
Hard to control the volume
Gel comes out of the tip making a mess
Assemble and disassemble is hard
Mixing tip cap is easy to lose
Customer

## Slide 2
Other Dispenser

## Slide 3
Summary of Brainstorm
Hard to control the volume
(10)
Control with vision
Control with tactility/Sound
Single use
Glue gun
Gel comes out of the tip making a mess
(10)
Quick closing
Internal and external spring
Pull back with bulge
One way valve
Reduce size of mixing tip
Mixing tip cap is easy to lose
(9)
Disposable dispenser
More tips or mixing tip caps
Integrate the cap to box
Connect the cap to syringe
Enlarge the cap
Assemble and disassemble is hard
(8)
One way valve
Integrate the mixing tip and syringe cap
Not pleasing
(13)
Cylinder outer box
Paint syringe
Electrical design
Future style
50 concepts total

## Slide 4
Concepts from Brainstorm
Concept-1 | Concept-2 | Concept-3
Concept-4 | Concept-5 | Concept-6
Concept-7 | Concept-8 | Concept-9/10

## Slide 5
Pugh Matrix Analysis
 | Screening Criteria | Ranking |  |  | Weight
 |  | 1 | 3 | 5 | 
Attractiveness | Mess avoid ability | The same as current syringe | User technique dependent | No mess | 17%
 | Volume Control/dosing | Dispense more than full dose | Full dose covering whole mouth piece but inconsistent distribution | Full dose with consistent distribution | 33%
 | Easy use(push force, number of steps, ergonomics and size | Compare them one by one and rank across 1-5 |  |  | 50%
Fit | Cost | More cost than current syringe (5X) | More cost than existing syringe (2.5X) | Comparable cost than existing syringe (1X) | 40%
 | Manufacturability | syringe with cosmetic shell and mechanism | syringe with cosmetic shell | syringe | 20%
 | Maturity | new mixing tip and no model and new mechanism no model | model new mixing tip, new mechanism with model simple possible | mixing tip and no new mechanism with more than two parts | 10%
 | Reliability | more than 2 components are not well understood | no more than 2 components are not well understood | all components are understood well | 30%

## Slide 6
Pugh Matrix Result
Chart: Concepts Ranking
| 2.4000000000000004
1 | 2.8333
2 | 3.8333
3 | 3.6667
4 | 2.8333
5 | 2.6667
6 | 3.5
7 | 2
8 | 5
9 | 1
10 | 1.6667

## Slide 7
Winners
Concept 2 | Concept 4

## Slide 8
Creo2 Model
Description:
Hypothesis:
Transfer function:
Enablers: it will work since:
Disabler: it might not work since:
Concept-2-multiuse
Pull-back spring cover
plunger
Dual barrel
Guide slot shell
bump

## Slide 9
Creo2 Model
Description:
Hypothesis:
Transfer function:
Enablers: it will work since:
Disabler: it might not work since:
Dual barrel
Concept-2-single use
plunger
Feedback piece
Guide slot shell

## Slide 10
Creo2 Model
Concept-4-single use
Description:
Hypothesis:
Transfer function:
Disabler: it might not work since:
Dual barrel
Plunger
Finger holder
Feedback piece
Feedback slot
Enablers: it will work since:

## Slide 11
Creo2 Model
Description:
Hypothesis:
Transfer function:
Enablers: it will work since:
Disabler:
Single use barrel
Cosmetics shell
Rolling wheel
Gear rack plunger
Concept-3

## Slide 12
3D Printing Model